## Slide 1: FAVPRO NRC’s New Probabilistic RPV Integrity Assessment Tool
Patrick Raynaud
Senior Materials Engineer
U.S. Nuclear Regulatory commission
Patrick.Raynaud@nrc.gov

## Slide 2: Disclaimer
This presentation was prepared as an account of work sponsored by an agency of the U.S. Government. Neither the U.S. Government nor any agency thereof, nor any of their employees, makes any warranty, expressed or implied, or assumes any legal liability or responsibility for any third party’s use, or the results of such use, of any information, apparatus, product, or process disclosed in this presentation, or represents that its use by such third party would not infringe privately owned rights. The views expressed in this paper are not necessarily those of the U.S. Nuclear Regulatory Commission.

## Slide 3: Acknowledgements
U.S. NRC
  Chris Ulmer, Chris Nellis
Archaeologic Inc.
  Damian Rouson, Karla Morris, Brad Richardson, Kate Rasmussen, Giovanni Facco
NUMARK Associates, Inc.
  Terry Dickson, Marvin Smith, Andrew Dyszel

## Slide 4: Past: FAVOR-v16.1
Developed and issued by ORNL late 2016
Legacy Fortran
FAVOR = FAVLOAD + FAVPFM + FAVPOST
  3 executables
  Information passed via formatted text files
Serial and sequential code
Software Quality Assurance (SQA) gaps
  ML20017A171
  ML20017A170

## Slide 5: Past: FAVOR-v16.1 SQA
Assessment of SQA documentation revealed gaps
  FAVOR was developed under ORNL SQA program, but documentation lost in time
What we had:
  Small integration test suite: 27 cases with poor coverage
  Theory and User manuals
  Many reports on FAVOR documenting its use and benchmarking
What was missing:
  SQA documentation
  Good descriptions of source code structure
  Source code version control

## Slide 6: Vision and Goals for FAVOR Modernization
Completely refactor the code to create an improved tool with equivalent capabilities, written in modern Fortran
GOALS
  Maintainability
  SQA and V&V improvements (testing and documentation)
  Modularity (make the code adaptable, enable easier feature addition)
  Modern programming:
    Object-oriented code
    Parallel code (performance improvements)
  Maximize automation for testing and documentation
  Merge the 3 sub-codes into 1 program: FAVPRO
  Use State-of-Practice tools and libraries
    GitHub: source control
    Fortran Package Manager for building and testing
    Veggies/Garden: unit testing framework
    Java Script Object Notation [JSON] for I/O

## Slide 7: Present: FAVOR-v20.1.12
CMake build system
Source code improvements:
  Convert to free form ‘.f90’ files
  Modularization
  Begin removal of obsolete Fortran
Testing improvements:
  New integration tests for better coverage (58 tests)
  A few unit tests
  Automatically run testing on GitHub for all code changes
Documentation
  Automatically generate developer documentation
    FORD: Fortran Documenter
    Detailed code descriptions from source parsing
  Created new SQA documents:
    SQAP: ML21180A161
    CMMP: ML21180A167
    SRD: ML21246A230
    SDD: ML22132A068
  Created new Manuals:
    User Manual: ML21175A301
    Theory Manual: ML21175A300

## Slide 8: Future: FAVPRO

## Slide 9: FAVPRO: Leveraging the Modern Fortran Ecosystem
Fortran has a growing user community and there is renewed interest in the language
Fortran 2018 is a modern object-oriented parallel programming language
  High performance for scientific and engineering computations (one of the best)
We use the following libraries
  fpm: Fortran Package Manager as the building and testing system
  veggies/garden for unit test development
  assert: assertion utility -> prerequisite checks
  quaff: quantities for Fortran -> unit tracking
  rojff: return of JSON for Fortran -> JSON interface
  erloff: errors and logging for Fortran
  iso_varying_string: implementation of Fortran ISO_VARYING_STRING

## Slide 10: FAVPRO: Development Status
JSON I/O mostly implemented (ongoing)
Full modularization complete
Refactoring ongoing: goal is 100% in the next year
  Corrected minor bugs with little impact on the results
Move towards object-oriented functional programming (ongoing)
Merge the 3 sub-programs to reduce/remove intermediate I/O (2/3 complete)
Parallelization: the last step (not yet started)

## Slide 11: FAVPRO Features: As-Found Flaw Population

## Slide 12: FAVPRO Features: Increased Use of ASME Standard

## Slide 13: FAVPRO Features: New Embrittlement Trend Curves (ETC)
Currently available ETC
  RG-1.99 Rev. 2
  EONY 2000 and 2006
    To be consolidated into latest EONY model (2013?)
  Kirk 2007, Radamo 2007, and Kirk+Radamo 2007
    Early versions of ASTM E-900 model: to be removed
Add ‘mainstream’ embrittlement trend curves to the FAVPRO options
  ASTM E-900
  Japanese model (update to JEAC4201, recently presented at FONTEVRAUD-10)
  French model (2011: FONTEVRAUD-7, or more recent if available)

## Slide 14: FAVOR/FAVPRO User Group
To obtain FAVOR and/or FAVPRO:
  Fill out the NRC Codes NDA
  Once approved, the code executables and input generator are downloaded via NRC’s BOX service
All approved users become members of the User Group
  Regular meetings (first meeting on 5/19/22-5/20/22), then short virtual updates (3-6 months), one longer meeting annually (format TBD)
  Newsletters
  New code versions
  User input to the development team is encouraged (bugs, new features, etc.)
Cost: free!
  Could change at some point, but not in immediate future
What about source code?
  Can be obtained on special case-by-case basis, pending approval of special request
Send any FAVOR/FAVPRO questions to Patrick.Raynaud@nrc.gov

## Slide 15: Summary and Perspectives
FAVPRO is a new tool to replace FAVOR
Enhanced SQA pedigree and testing
Modern, modular, parallel code for enhanced performance, enhanced user experience, and enhanced adaptability
New features:
  As-found flaw modeling
  Standard conforming K solutions where possible (ASME)
  New embrittlement trend curves to reflect the latest standards and research
FAVPRO is a robust and resilient foundation that can be built upon to add new models, new probabilistic functionality, new materials, and new physical models to adapt to the rapidly evolving nuclear technology landscape

## Slide 16: For questions about FAVPRO Patrick.Raynaud@nrc.gov